## Slide 1
Positron Identification by Coincident Annihilation Photons (PICAP) system
B.B. Bickford
Faculty advisors - May-Win Thein, J.J. Connell
C. Lopate D. L. Tran, Space Science Center University of New Hampshire
Abstract
This concept is a new method for detecting moderate energy positrons and negatron in space. The current method for measuring these particles is by using a magnet spectrometer. Magnet spectrometers typically weigh greater than 10 kg, use more than 10 watts of power and require a magnet. The goal of the proposed PICAP design is to reduce these resources to provide an alternative, and more attractive space flight instrument. We estimate a flight instrument to have a weight less than 4 kg, power draw of less than 3 Watts and no magnet. As a space flight instrument this resource allotment will would make the PICAP instrument a much more desirable alternative.
Methods
The PICAP instrument works by first using the dE/dx method versus residual energy technique to identify incoming particles. Positrons within the appropriate energy range will annihilate in the scintillation material and produce coincidental 511 keV photons. These annihilation photons are then detected by two of the four surrounding annular sections of crystal scintillators. Unwanted particle data, particles not entering through top window, will be identified by using scintillation material all around the instrument along with a large solid state detector at the bottom of the device.
Instrument Concept and Design
C- Center scintillation material (PTV)
G- Heavy scintillation material (BGO)
D- Solid state detectors
S- Plastic scintillation material (PTV)
Background and Project Goal
New design for detecting and distinguishing energetic positrons (anti electrons) from negatrons (ordinary electrons) in space
Design, build, and test a proof of principle prototype telescope
Future plans
Finish fabrications
Test at the Idaho State cyclotron, and Mass General Hospital proton beam
References
Connell, J., J. Kalainoff, and C. Lopate. "Design Concept and Modeling of a New Positron Identification by Coincident Annihilation Photons (PICAP) System." Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 593.3 (2008): 431-39. Print.
Side cross section view of concept design
Top cross section view of concept design
Side cross section view of Mechanical design
Top cross section view of Mechanical design
CAD model of PICAP instrument
Design Constraints
  Light tight - This instrument was designed to exclude all ambient light
  Reflecting light -Teflon was used around scintillators to reflect light towards the opening face of the photo multiplier tubes
  Cross talk – Teflon and Aluminum was used around each of the scintillators to ensure light would not cross from one to another
  7 Circuit boards and corresponding wires had to be included for the photomultiplier tubes and solid state detectors
  Purging – purge ports were required to exclude contamination
  Instrument was required to act as a faraday cage in order to exclude electromagnetic interference
  Designed with Assembly + Disassembly capabilities
Notes
39 different fabricated parts
designed from stock material sizes
flight instrument will have significantly fewer but much more complex parts
7 Photomultiplier tubes (PMT) and corresponding dynode circuit boards
4 Solid-State detectors
Materials; Aluminum, Teflon,
BGO, PVT, Delrin, Brass foil
Space flight instrument will be fabricated with magnesium rather than aluminum, this is expected to drop the total weight by roughly 1 kg
Testing and Analysis
Venting analysis - to ensure the change in pressure between the inside and outside of the
telescope won't have adverse effects such as structural failures or separations of joined parts.
  A ventilation area of 2.31 cm^2 is required for flight instrument
Gamma ray absorption probability - calculations were performed to determine the required thickness of the scintillator based on the material
  Thickness required for annular sections: BGO .94cm
CsI 2.3cm
Thermal Analysis - was done to model the telescope with the effects of temperature due to
radiation from the sun
  Max temperature allowed 383 K (110 C°)
  Max temperature found 331 K (58 C°)
Vibration simulations - FEA software was used to find the natural frequencies of the telescope
  Greater then 50 Hz is required for flight instrument
  First five natural frequencies (Hz):
1277.7 | 1286.4 | 2070.6 | 2484.5 | 4055
Dimensions of prototype |  |  | 
Total Height | 16.78 cm | Total mass | 3.3 kg
Total width | 22.47 cm | Total Volume | 1985 cm^3
PMT
PMT
PMT
PMT
D1
D2
D3
D4